## Slide 1: Computer Organization And Architecture
Al Bashir
Lecturer, Dept. of CSE
Dhaka International University
CSE-209
Lecture - 02

## Slide 2: ENIAC
ENIAC The ENIAC (Electronic Numerical Integrator And Computer), designed and constructed at the University of Pennsylvania, was the world’s first general purpose electronic digital computer. The project was a response to U.S. needs during
World War II.

## Slide 3: ENIAC Cont.…
The Army’s Ballistics Research Laboratory (BRL), an agency responsible for developing range and trajectory tables for new weapons, was having difficulty supplying these tables accurately and within a reasonable time frame. Without these firing tables, the new weapons and artillery were useless to gunners. The BRL employed more than 200 people who, using desktop calculators, solved the necessary ballistics equations. Preparation of the tables for a single weapon would take one person many hours, even days.

## Slide 4: ENIAC - background
Electronic Numerical Integrator And Computer
Eckert and Mauchly
University of Pennsylvania
Trajectory tables for weapons
Started 1943
Finished 1946
  Too late for war effort
Used until 1955

## Slide 5: ENIAC - details
Decimal (not binary)
20 accumulators of 10 digits
Programmed manually by switches
18,000 vacuum tubes
30 tons
15,000 square feet
140 kW power consumption
5,000 additions per second

## Slide 6: von Neumann/Turing (IAS Computer)
In 1946, von Neumann and his colleagues began the design of a new stored program computer, referred to as the IAS computer, at the Princeton Institute for Advanced Studies. The IAS computer, although not completed until 1952, is the prototype of all subsequent general-purpose computers.

## Slide 7: von Neumann/Turing
Stored Program concept
Main memory storing programs and data
ALU operating on binary data
Control unit interpreting instructions from memory and executing
Input and output equipment operated by control unit
Princeton Institute for Advanced Studies
  IAS
Completed 1952

## Slide 8: Structure of von Neumann machine

## Slide 9: IAS - details
1000 x 40 bit words
  Binary number
  2 x 20 bit instructions
Set of registers (storage in CPU)
  Memory Buffer Register
  Memory Address Register
  Instruction Register
  Instruction Buffer Register
  Program Counter
  Accumulator
  Multiplier Quotient

## Slide 10: IAS – Memory Format

## Slide 11: Structure of IAS – detail

## Slide 12: Structure of IAS – detail
• Memory buffer register (MBR): Contains a word to be stored in memory or sent to the I/O unit, or is used to receive a word from memory or from the I/O unit.
• Memory address register (MAR): Specifies the address in memory of the word to be written from or read into the MBR.
• Instruction register (IR): Contains the 8-bit opcode instruction being executed.

## Slide 13: Structure of IAS – detail
•Instruction buffer register (IBR): Employed to hold temporarily the righthand instruction from a word in memory.
• Program counter (PC): Contains the address of the next instruction-pair to be fetched from memory.
• Accumulator (AC) and multiplier quotient (MQ):Employed to hold temporarily operands and results of ALU operations. For example, the result of multiplying two 40-bit numbers is an 80-bit number; the most significant 40 bits are stored in the AC and the least significant in the MQ.

## Slide 14: IAS – Instruction Set

## Slide 15: Commercial Computers
1947 - Eckert-Mauchly Computer Corporation
UNIVAC I (Universal Automatic Computer)
US Bureau of Census 1950 calculations
Became part of Sperry-Rand Corporation
Late 1950s - UNIVAC II
  Faster
  More memory

## Slide 16: IBM
Punched-card processing equipment
1953 - the 701
  IBM’s first stored program computer
  Scientific calculations
1955 - the 702
  Business applications
Lead to 700/7000 series

## Slide 17: Transistors
Replaced vacuum tubes
Smaller
Cheaper
Less heat dissipation
Solid State device
Made from Silicon (Sand)
Invented 1947 at Bell Labs
William Shockley et al.

## Slide 18: Transistor Based Computers
Second generation machines
NCR & RCA produced small transistor machines
IBM 7000
DEC - 1957
  Produced PDP-1

## Slide 19: Microelectronics
Literally - “small electronics”
A computer is made up of gates, memory cells and interconnections
These can be manufactured on a semiconductor
e.g. silicon wafer

## Slide 20: Generations of Computer
Vacuum tube - 1946-1957
Transistor - 1958-1964
Small scale integration - 1965 on
  Up to 100 devices on a chip
Medium scale integration - to 1971
  100-3,000 devices on a chip
Large scale integration - 1971-1977
  3,000 - 100,000 devices on a chip
Very large scale integration - 1978 -1991
  100,000 - 100,000,000 devices on a chip
Ultra large scale integration – 1991 -
  Over 100,000,000 devices on a chip

## Slide 21: Moore’s Law
Increased density of components on chip
Gordon Moore – co-founder of Intel
Number of transistors on a chip will double every year
Since 1970’s development has slowed a little
  Number of transistors doubles every 18 months
Cost of a chip has remained almost unchanged
Higher packing density means shorter electrical paths, giving higher performance
Smaller size gives increased flexibility
Reduced power and cooling requirements
Fewer interconnections increases reliability

## Slide 22: Growth in CPU Transistor Count

## Slide 23: IBM 360 series
1964
Replaced (& not compatible with) 7000 series
First planned “family” of computers
  Similar or identical instruction sets
  Similar or identical O/S
  Increasing speed
  Increasing number of I/O ports (i.e. more terminals)
  Increased memory size
  Increased cost
Multiplexed switch structure

## Slide 24: DEC PDP-8
1964
First minicomputer (after miniskirt!)
Did not need air conditioned room
Small enough to sit on a lab bench
$16,000
  $100k+ for IBM 360
Embedded applications & OEM
BUS STRUCTURE

## Slide 25: DEC - PDP-8 Bus Structure

## Slide 26: Semiconductor Memory
1970
Fairchild
Size of a single core
  i.e. 1 bit of magnetic core storage
Holds 256 bits
Non-destructive read
Much faster than core
Capacity approximately doubles each year

## Slide 27: Intel
1971 - 4004
  First microprocessor
  All CPU components on a single chip
  4 bit
Followed in 1972 by 8008
  8 bit
  Both designed for specific applications
1974 - 8080
  Intel’s first general purpose microprocessor

## Slide 28: Speeding it up
Pipelining
On board cache
On board L1 & L2 cache
Branch prediction
Data flow analysis
Speculative execution

## Slide 29: Performance Balance
Processor speed increased
Memory capacity increased
Memory speed lags behind processor speed

## Slide 30: Login and Memory Performance Gap

## Slide 31: Solutions
Increase number of bits retrieved at one time
  Make DRAM “wider” rather than “deeper”
Change DRAM interface
  Cache
Reduce frequency of memory access
  More complex cache and cache on chip
Increase interconnection bandwidth
  High speed buses
  Hierarchy of buses

## Slide 32: I/O Devices
Peripherals with intensive I/O demands
Large data throughput demands
Processors can handle this
Problem moving data
Solutions:
  Caching
  Buffering
  Higher-speed interconnection buses
  More elaborate bus structures
  Multiple-processor configurations

## Slide 33: Typical I/O Device Data Rates

## Slide 34: Key is Balance
Processor components
Main memory
I/O devices
Interconnection structures

## Slide 35: Improvements in Chip Organization and Architecture
Increase hardware speed of processor
  Fundamentally due to shrinking logic gate size
    More gates, packed more tightly, increasing clock rate
    Propagation time for signals reduced
Increase size and speed of caches
  Dedicating part of processor chip
    Cache access times drop significantly
Change processor organization and architecture
  Increase effective speed of execution
  Parallelism

## Slide 36: Problems with Clock Speed and Login Density
Power
  Power density increases with density of logic and clock speed
  Dissipating heat
RC delay
  Speed at which electrons flow limited by resistance and capacitance of metal wires connecting them
  Delay increases as RC product increases
  Wire interconnects thinner, increasing resistance
  Wires closer together, increasing capacitance
Memory latency
  Memory speeds lag processor speeds
Solution:
  More emphasis on organizational and architectural approaches

## Slide 37: Intel Microprocessor Performance

## Slide 38: Increased Cache Capacity
Typically two or three levels of cache between processor and main memory
Chip density increased
  More cache memory on chip
    Faster cache access
Pentium chip devoted about 10% of chip area to cache
Pentium 4 devotes about 50%

## Slide 39: More Complex Execution Logic
Enable parallel execution of instructions
Pipeline works like assembly line
  Different stages of execution of different instructions at same time along pipeline
Superscalar allows multiple pipelines within single processor
  Instructions that do not depend on one another can be executed in parallel

## Slide 40: Diminishing Returns
Internal organization of processors complex
  Can get a great deal of parallelism
  Further significant increases likely to be relatively modest
Benefits from cache are reaching limit
Increasing clock rate runs into power dissipation problem
  Some fundamental physical limits are being reached

## Slide 41: New Approach – Multiple Cores
Multiple processors on single chip
  Large shared cache
Within a processor, increase in performance proportional to square root of increase in complexity
If software can use multiple processors, doubling number of processors almost doubles performance
So, use two simpler processors on the chip rather than one more complex processor
With two processors, larger caches are justified
  Power consumption of memory logic less than processing logic

## Slide 42: x86 Evolution (1)
8080
  first general purpose microprocessor
  8 bit data path
  Used in first personal computer – Altair
8086 – 5MHz – 29,000 transistors
  much more powerful
  16 bit
  instruction cache, prefetch few instructions
  8088 (8 bit external bus) used in first IBM PC
80286
  16 Mbyte memory addressable
  up from 1Mb
80386
  32 bit
  Support for multitasking
80486
  sophisticated powerful cache and instruction pipelining
  built in maths co-processor

## Slide 43: x86 Evolution (2)
Pentium
  Superscalar
  Multiple instructions executed in parallel
Pentium Pro
  Increased superscalar organization
  Aggressive register renaming
  branch prediction
  data flow analysis
  speculative execution
Pentium II
  MMX technology
  graphics, video & audio processing
Pentium III
  Additional floating point instructions for 3D graphics

## Slide 44: x86 Evolution (3)
Pentium 4
  Note Arabic rather than Roman numerals
  Further floating point and multimedia enhancements
Core
  First x86 with dual core
Core 2
  64 bit architecture
Core 2 Quad – 3GHz – 820 million transistors
  Four processors on chip
x86 architecture dominant outside embedded systems
Organization and technology changed dramatically
Instruction set architecture evolved with backwards compatibility
~1 instruction per month added
500 instructions available
See Intel web pages for detailed information on processors

## Slide 45: Embedded Systems ARM
ARM evolved from RISC design
Used mainly in embedded systems
  Used within product
  Not general purpose computer
  Dedicated function
  E.g. Anti-lock brakes in car

## Slide 46: Embedded Systems Requirements
Different sizes
  Different constraints, optimization, reuse
Different requirements
  Safety, reliability, real-time, flexibility, legislation
  Lifespan
  Environmental conditions
  Static v dynamic loads
  Slow to fast speeds
  Computation v I/O intensive
  Descrete event v continuous dynamics

## Slide 47: Possible Organization of an Embedded System

## Slide 48: ARM Evolution
Designed by ARM Inc., Cambridge, England
Licensed to manufacturers
High speed, small die, low power consumption
PDAs, hand held games, phones
  E.g. iPod, iPhone
Acorn produced ARM1 & ARM2 in 1985 and ARM3 in 1989
Acorn, VLSI and Apple Computer founded ARM Ltd.

## Slide 49: ARM Systems Categories
Embedded real time
Application platform
  Linux, Palm OS, Symbian OS, Windows mobile
Secure applications

## Slide 50: Performance Assessment Clock Speed
Key parameters
  Performance, cost, size, security, reliability, power consumption
System clock speed
  In Hz or multiples of
  Clock rate, clock cycle, clock tick, cycle time
Signals in CPU take time to settle down to 1 or 0
Signals may change at different speeds
Operations need to be synchronised
Instruction execution in discrete steps
  Fetch, decode, load and store, arithmetic or logical
  Usually require multiple clock cycles per instruction
Pipelining gives simultaneous execution of instructions
So, clock speed is not the whole story

## Slide 51: System Clock

## Slide 52: Instruction Execution Rate
Millions of instructions per second (MIPS)
Millions of floating point instructions per second (MFLOPS)
Heavily dependent on instruction set, compiler design, processor implementation, cache & memory hierarchy

## Slide 53: Benchmarks
Programs designed to test performance
Written in high level language
  Portable
Represents style of task
  Systems, numerical, commercial
Easily measured
Widely distributed
E.g. System Performance Evaluation Corporation (SPEC)
  CPU2006 for computation bound
    17 floating point programs in C, C++, Fortran
    12 integer programs in C, C++
    3 million lines of code
  Speed and rate metrics
    Single task and throughput

## Slide 54: SPEC Speed Metric
Single task
Base runtime defined for each benchmark using reference machine
Results are reported as ratio of reference time to system run time
  Trefi execution time for benchmark i on reference machine
  Tsuti execution time of benchmark i on test system
Overall performance calculated by averaging ratios for all 12 integer benchmarks
  Use geometric mean
    Appropriate for normalized numbers such as ratios

## Slide 55: SPEC Rate Metric
Measures throughput or rate of a machine carrying out a number of tasks
Multiple copies of benchmarks run simultaneously
  Typically, same as number of processors
Ratio is calculated as follows:
  Trefi reference execution time for benchmark i
  N number of copies run simultaneously
  Tsuti elapsed time from start of execution of program on all N processors until completion of all copies of program
  Again, a geometric mean is calculated

## Slide 56: Amdahl’s Law
Gene Amdahl [AMDA67]
Potential speed up of program using multiple processors
Concluded that:
  Code needs to be parallelizable
  Speed up is bound, giving diminishing returns for more processors
Task dependent
  Servers gain by maintaining multiple connections on multiple processors
  Databases can be split into parallel tasks

## Slide 57: Amdahl’s Law Formula
Conclusions
  f small, parallel processors has little effect
  N ->∞, speedup bound by 1/(1 – f)
    Diminishing returns for using more processors
For program running on single processor
  Fraction f of code infinitely parallelizable with no scheduling overhead
  Fraction (1-f) of code inherently serial
  T is total execution time for program on single processor
  N is number of processors that fully exploit parralle portions of code

## Slide 58: Internet Resources
http://www.intel.com/
  Search for the Intel Museum
http://www.ibm.com
http://www.dec.com
Charles Babbage Institute
PowerPC
Intel Developer Home

## Slide 59: References
AMDA67 Amdahl, G. “Validity of the Single-Processor Approach to Achieving Large-Scale Computing Capability”, Proceedings of the AFIPS Conference, 1967.

## Slide 60
Question??

## Slide 61
Thanks