## Slide 1: Computer Organization And Architecture
Al Bashir
Lecturer, Dept. of CSE
Dhaka International University
CSE-209
Lecture - 04

## Slide 2: Content
Computer Function
Instruction Fetch and Execute
Interrupts
Interconnection Structure
Bus Interconnection

## Slide 3: What is a program?
A sequence of steps
For each step, an arithmetic or logical operation is done
For each operation, a different set of control signals is needed

## Slide 4: What is a program?
A computer program is a collection of instructions that performs a specific task when executed by a computer. A computer requires programs to function.

## Slide 5: Function of Control Unit
For each operation a unique code is provided
  e.g. ADD, MOVE
A hardware segment accepts the code and issues the control signals
We have a computer!

## Slide 6: Function of Control Unit : Components
The Control Unit and the Arithmetic and Logic Unit constitute the Central Processing Unit
Data and instructions need to get into the system and results out
  Input/output
Temporary storage of code and results is needed
  Main memory

## Slide 7: Computer Components: Top Level View

## Slide 8: Instruction Fetch and Execute
At the beginning of each instruction cycle, the processor fetches an instruction from memory.
In a typical processor, a register called the program counter (PC) holds the address of the instruction to be fetched next.
Unless told otherwise, the processor always increments the PC after each instruction fetch so that it will fetch the next instruction in sequence (i.e., the instruction located at the next higher memory address).

## Slide 9: Instruction Cycle
Two steps:
  Fetch
  Execute

## Slide 11: Fetch Cycle
Program Counter (PC) holds address of next instruction to fetch
Processor fetches instruction from memory location pointed to by PC
Increment PC
  Unless told otherwise
Instruction loaded into Instruction Register (IR)
Processor interprets instruction and performs required actions

## Slide 12: Execute Cycle
Processor-memory
  data transfer between CPU and main memory
Processor I/O
  Data transfer between CPU and I/O module
Data processing
  Some arithmetic or logical operation on data
Control
  Alteration of sequence of operations
  e.g. jump
Combination of above

## Slide 13: Example of Program Execution

## Slide 14: Example of Program Execution cont…
Program counter (PC) = Address of instruction
Instruction register (IR) = Instruction being executed
Accumulator (AC) = Temporary storage
0001 = Load AC from memory
0010 = Store AC to memory
0101 = Add to AC from memory

## Slide 15: Example of Program Execution cont…
The program fragment shown adds the contents of the memory word at address 940 to the contents of the memory word at address 941 and stores the result in the latter location. Three instructions, which can be described as three fetch and three execute cycles, are required:

## Slide 16: Example of Program Execution cont…
1. The PC contains 300, the address of the first instruction. This instruction (the value 1940 in hexadecimal) is loaded into the instruction register IR and the PC is incremented. Note that this process involves the use of a memory address register (MAR) and a memory buffer register (MBR). For simplicity, these intermediate registers are ignored.
2. The first 4 bits (first hexadecimal digit) in the IR indicate that the AC is to be loaded. The remaining 12 bits (three hexadecimal digits) specify the address (940) from which data are to be loaded.
3. The next instruction (5941) is fetched from location 301 and the PC is incremented.
4. The old contents of the AC and the contents of location 941 are added and the result is stored in the AC.
5. The next instruction (2941) is fetched from location 302 and the PC is incremented.
6. The contents of the AC are stored in location 941.

## Slide 17: Instruction Cycle State Diagram

## Slide 18: Instruction Cycle State Diagram
Instruction address calculation (iac): Determine the address of the next instruction to be executed. Usually, this involves adding a fixed number to the address of the previous instruction.
Instruction fetch (if): Read instruction from its memory location into the processor.
Instruction operation decoding (iod): Analyze instruction to determine type of operation to be performed and operand(s) to be used.
Operand address calculation (oac): If the operation involves reference to an operand in memory or available via I/O, then determine the address of the operand.
Operand fetch (of): Fetch the operand from memory or read it in from I/O.
Data operation (do): Perform the operation indicated in the instruction.
Operand store (os): Write the result into memory or out to I/O.

## Slide 19: Interrupts
Mechanism by which other modules (e.g. I/O) may interrupt normal sequence of processing
Program
  e.g. overflow, division by zero
Timer
  Generated by internal processor timer
  Used in preemptive multi-tasking
I/O
  from I/O controller
Hardware failure
  e.g. memory parity error

## Slide 20: Interrupts : Program Flow Control

## Slide 21: Program Timing : Short I/O Wait

## Slide 22: Program Timing : Long I/O Wait

## Slide 23: Interrupts Cycle
Added to instruction cycle
Processor checks for interrupt
  Indicated by an interrupt signal
If no interrupt, fetch next instruction
If interrupt pending:
  Suspend execution of current program
  Save context
  Set PC to start address of interrupt handler routine
  Process interrupt
  Restore context and continue interrupted program

## Slide 24: Transfer of Control via Interrupts

## Slide 25: Instruction Cycle with Interrupts

## Slide 26: Instruction Cycle (with Interrupts) - State Diagram

## Slide 27: Connecting
All the units must be connected
Different type of connection for different type of unit
  Memory
  Input/Output
  CPU

## Slide 28: Connecting : Computer Modules

## Slide 29: Memory Connection
Receives and sends data
Receives addresses (of locations)
Receives control signals
  Read
  Write
  Timing

## Slide 30: Input/Output Connection
Similar to memory from computer’s viewpoint
Output
  Receive data from computer
  Send data to peripheral
Input
  Receive data from peripheral
  Send data to computer

## Slide 31: Input/Output Connection Cont..
Receive control signals from computer
Send control signals to peripherals
  e.g. spin disk
Receive addresses from computer
  e.g. port number to identify peripheral
Send interrupt signals (control)

## Slide 32: CPU Connection
Reads instruction and data
Writes out data (after processing)
Sends control signals to other units
Receives (& acts on) interrupts

## Slide 33: Inter Connection Must Support….
Memory to processor: The processor reads an instruction or a unit of data from memory.
Processor to memory: The processor writes a unit of data to memory.
I/O to processor:The processor reads data from an I/O device via an I/O module.
Processor to I/O: The processor sends data to the I/O device.
I/O to or from memory: For these two cases, an I/O module is allowed to exchange data directly with memory, without going through the processor, using direct memory access (DMA).

## Slide 34: Buses
There are a number of possible interconnection systems
Single and multiple BUS structures are most common
e.g. Control/Address/Data bus (PC)
e.g. Unibus (DEC-PDP)

## Slide 35: What is Bus?
A communication pathway connecting two or more devices.
A bus is a communication pathway connecting two or more devices.
Typically, a bus consists of multiple communication pathways, or lines. Each line is capable of transmitting signals representing binary 1 and binary 0. Over time, a sequence of binary digits can be transmitted across a single line. Taken together, several lines of a bus can be used to transmit binary digits simultaneously (in parallel).
For example, an 8-bit unit of data can be transmitted over eight bus lines.

## Slide 36: Bus Interconnection Scheme

## Slide 37: Data Bus
The data lines provide a path for moving data among system modules. These lines, collectively, are called the data bus. The data bus may consist of 32, 64, 128, or even more separate lines, the number of lines being referred to as the width of the data bus. Because each line can carry only 1 bit at a time, the number of lines determines how many bits can be transferred at a time.
Carries data
  Remember that there is no difference between “data” and “instruction” at this level
Width is a key determinant of performance
  8, 16, 32, 64 bit

## Slide 38: Address Bus
The address lines are used to designate the source or destination of the data on the data bus. For example, if the processor wishes to read a word (8, 16, or 32 bits) of data from memory, it puts the address of the desired word on the address lines.
Clearly, the width of the address bus determines the maximum possible memory capacity of the system.
Identify the source or destination of data
e.g. CPU needs to read an instruction (data) from a given location in memory
Bus width determines maximum memory capacity of system
  e.g. 8080 has 16 bit address bus giving 64k address space

## Slide 39: Control Bus
The control lines are used to control the access to and the use of the data and address lines. Because the data and address lines are shared by all components, there must be a means of controlling their use.
Control signals transmit both command and timing information among system modules.
Control and timing information
  Memory read/write signal
  Interrupt request
  Clock signals

## Slide 40: Physical Realization of Bus Architecture

## Slide 41: Bus Types
Dedicated
  Separate data & address lines
Multiplexed
  Shared lines
  Address valid or data valid control line
  Advantage - fewer lines
  Disadvantages
    More complex control
    Ultimate performance

## Slide 42
Question??

## Slide 43
Thanks