## Slide 1: Computer Organization And Architecture
Al Bashir
Lecturer, Dept. of CSE
Dhaka International University
CSE-209
Lecture – 05+06

## Slide 2: Content
Computer Memory System Overview
Cache Memory Principles
Elements of Cache Design

## Slide 3: Computer memory
In computing, memory refers to the computer hardware integrated circuits that store information for immediate use in a computer; it is synonymous with the term "primary storage".
Computer memory operates at a high speed, for example random-access memory (RAM), as a distinction from storage that provides slow-to-access information but offers higher capacities. If needed, contents of the computer memory can be transferred to secondary storage, through a memory management technique called "virtual memory".
-- Wikipedia

## Slide 4: Computer memory
Key Characteristics of Computer Memory Systems
Location
  Internal (e.g. processor registers, main memory, cache)
  External (e.g. optical disks, magnetic disks, tapes)
Capacity
  Number of words
  Number of bytes
Unit of Transfer
  Word
  Block
Access Method
  Sequential
  Direct
  Random
  Associative

## Slide 5: Computer memory
Key Characteristics of Computer Memory Systems
Performance
  Access time
  Cycle time
  Transfer rate
Physical Type
  Semiconductor
  Magnetic
  Optical
  Magneto-optical
Physical Characteristics
  Volatile/nonvolatile
  Erasable/nonerasable
Organization
  Memory modules

## Slide 6: Computer memory
Another definition is:
Computer memory is any physical device capable of storing information temporarily or permanently.

## Slide 7: The Memory Hierarchy
The design constraints on a computer’s memory can be summed up by three questions:
  How much?
  How fast?
  How expensive?
As might be expected, there is a trade-off among the three key characteristics of memory: namely- capacity, access time, and cost.
  • Faster access time, greater cost per bit
  • Greater capacity, smaller cost per bit
  • Greater capacity, slower access time

## Slide 8: The Memory Hierarchy
A typical hierarchy is illustrated in following Fig. As one goes down the hierarchy, the following occur:
Decreasing cost per bit
Increasing capacity
Increasing access time
Decreasing frequency of access of the memory by the processor

## Slide 9: Memory Hierarchy - Diagram

## Slide 10: Memory Hierarchy
Registers
  In CPU
Internal or Main memory
  May include one or more levels of cache
  “RAM”
External memory
  Backing store

## Slide 11: Hierarchy List
Registers
L1 Cache
L2 Cache
L3 Cache
Main memory
Disk cache
Disk
Optical
Tape

## Slide 12: Cache Memory
As CPU has to fetch instruction from main memory speed of CPU depending on fetching speed from main memory. CPU contains register which has fastest access but they are limited in number as well as costly. Cache is cheaper so we can access cache. Cache memory is a very high speed memory that is placed between the CPU and main memory, to operate at the speed of the CPU.
It is used to reduce the average time to access data from the main memory. The cache is a smaller and faster memory which stores copies of the data from frequently used main memory locations.

## Slide 13: Cache and Main Memory

## Slide 14: Why Cache Memory?
There is a relatively large and slow main memory together with a smaller, faster cache memory. The cache contains a copy of portions of main memory.
When the processor attempts to read a word of memory, a check is made to determine if the word is in the cache. If so, the word is delivered to the processor.
If not, a block of main memory, consisting of some fixed number of words, is read into the cache and then the word is delivered to the processor.

## Slide 15: Cache/Main Memory Structure

## Slide 16: Cache/Main Memory Structure
Main memory consists of up to 2n addressable words, with each word having a unique n-bit address.
For mapping purposes, this memory is considered to consist of a number of fixed length blocks of K words each. That is, there are M=2n/K blocks in main memory.
The cache consists of m blocks, called lines[1]. Each line contains K words, plus a tag of a few bits.
[1]In referring to the basic unit of the cache, the term line is used, rather than the term block, for two reasons:
to avoid confusion with a main memory block, which contains the same number of data words as a cache line; and
(2) because a cache line includes not only K words of data, just as a main memory block, but also include tag and control bits.

## Slide 17: Cache Read Operation
The processor generates the read address (RA) of a word to be read.
If the word is contained in the cache, it is delivered to the processor.
Otherwise, the block containing that word is loaded into the cache, and the word is delivered to the processor.

## Slide 18: Cache Read Operation - Flowchart

## Slide 19: Cache Organizations
The cache connects to the processor via data, control, and address lines.
The data and address lines also attach to data and address buffers, which attach to a system bus from which main memory is reached.
When a cache hit occurs, the data and address buffers are disabled and communication is only between processor and cache, with no system bus traffic.
When a cache miss occurs, the desired address is loaded onto the system bus and the data are returned through the data buffer to both the cache and the processor.

## Slide 20: Cache Organizations
.

## Slide 21: Elements of Cache Design
Cache Addresses
  Logical
  Physical
Cache Size
Mapping Function
  Direct
  Associative
  Set Associative
Replacement Algorithm
  Least recently used (LRU)
  First in first out (FIFO)
  Least frequently used (LFU)
  Random

## Slide 22: Elements of Cache Design cont…
Write Policy
  Write through
  Write back
  Write once
Line Size
Number of caches
  Single, two or more level
  Unified or split

## Slide 23: Mapping Function
Because there are fewer cache lines than main memory blocks, an algorithm is needed for mapping main memory blocks into cache lines.
Further, a means is needed for determining which main memory block currently occupies a cache line.
Three techniques can be used:
  Direct
  Associative and
  Set associative

## Slide 24: Direct Mapping
The simplest technique, known as direct mapping, maps each block of main memory into only one possible cache line.
The mapping is expressed as-
i = j modulo m
where
  i = cache line number
  j = main memory block number
  m = number of lines in the cache

## Slide 25: Direct Mapping
Figure shows the mapping for the first m blocks of main memory. Each block of main memory maps into one unique line of the cache.

## Slide 26: Direct Mapping : Cache Line Table
The next m blocks of main memory map into the cache in the same fashion; that is, block Bm of main memory maps into line L0 of cache, block Bm1 maps into line L1, and so on.
i = j modulo m
Cache line | Main Memory blocks held
0 | 0, m, 2m, 3m…2s-m
1 | 1,m+1, 2m+1…2s-m+1
… | 
m-1 | m-1, 2m-1,3m-1…2s-1

## Slide 27
Question??

## Slide 28
Thanks