## Slide 1: Computer Organization And Architecture
Al Bashir
Lecturer, Dept. of CSE
Dhaka International University
CSE-209
Lecture – 08

## Slide 2: Content
Set Associative Mapping
Pentium-4 cache architecture

## Slide 3: Set Associative Mapping
Cache is divided into a number of sets
Each set contains a number of lines
A given block maps to any line in a given set
  e.g. Block B can be in any line of set i
e.g. 2 lines per set
  2 way associative mapping
  A given block can be in one of 2 lines in only one set

## Slide 4: Set Associative Mapping Example
13 bit set number
Block number in main memory is modulo 213
000000, 00A000, 00B000, 00C000 … map to same set

## Slide 5: Mapping From Main Memory to Cache: v Associative

## Slide 6: Mapping From Main Memory to Cache: k-way Associative

## Slide 7: K-Way Set Associative Cache Organization

## Slide 8: Set Associative Mapping Address Structure
Use set field to determine cache set to look in
Compare tag field to see if we have a hit
e.g
  Address Tag Data Set number
  1FF 7FFC 1FF 12345678 1FFF
  001 7FFC 001 11223344 1FFF
Tag 9 bit
Set 13 bit
Word
2 bit

## Slide 9: Set Associative Mapping Summary
Address length = (s + w) bits
Number of addressable units = 2s+w words or bytes
Block size = line size = 2w words or bytes
Number of blocks in main memory = 2s
Number of lines in set = k
Number of sets = v = 2d
Number of lines in cache = kv = k * 2d
Size of tag = (s – d) bits

## Slide 10: Intel Cache Evolution
Problem
Solution
Processor on which feature first appears
External memory slower than the system bus.
Add external cache using faster memory technology.
386
Increased processor speed results in external bus becoming a bottleneck for cache access.
Move external cache on-chip, operating at the same speed as the processor.
486
Internal cache is rather small, due to limited space on chip
Add external L2 cache using faster technology than main memory
486
Contention occurs when both the Instruction Prefetcher and the Execution Unit simultaneously require access to the cache. In that case, the Prefetcher is stalled while the Execution Unit’s data access takes place.
Create separate data and instruction caches.
Pentium
Increased processor speed results in external bus becoming a bottleneck for L2 cache access.
Create separate back-side bus that runs at higher speed than the main (front-side) external bus. The BSB is dedicated to the L2 cache.
Pentium Pro
Move L2 cache on to the processor chip.
Pentium II
Some applications deal with massive databases and must have rapid access to large amounts of data. The on-chip caches are too small.
Add external L3 cache.
Pentium III
Move L3 cache on-chip.
Pentium 4

## Slide 11: Pentium 4 Block Diagram

## Slide 12: Pentium 4 Core Processor
Fetch/Decode Unit
  Fetches instructions from L2 cache
  Decode into micro-ops
  Store micro-ops in L1 cache
Out of order execution logic
  Schedules micro-ops
  Based on data dependence and resources
  May speculatively execute
Execution units
  Execute micro-ops
  Data from L1 cache
  Results in registers
Memory subsystem
  L2 cache and systems bus

## Slide 13: Pentium 4 Design Reasoning
Decodes instructions into RISC like micro-ops before L1 cache
Micro-ops fixed length
  Superscalar pipelining and scheduling
Pentium instructions long & complex
Performance improved by separating decoding from scheduling & pipelining
  (More later – ch14)
Data cache is write back
  Can be configured to write through
L1 cache controlled by 2 bits in register
  CD = cache disable
  NW = not write through
  2 instructions to invalidate (flush) cache and write back then invalidate
L2 and L3 8-way set-associative
  Line size 128 bytes

## Slide 14
Question??

## Slide 15
Thanks