## Slide 1: Bit rate and Baud rate
Bit rate is a measure of the number of data bits (that's 0's and 1's) transmitted in one second.
Baud rate (signal unit/sec: baud / sec: baud)
  the number of signal units per second
  less than or equal to the bit rate

## Slide 2: Example:1
An analog signal carries 4 bits in each signal unit. If 1000 signal units are sent per second, find the baud rate and the bit rate
Sol:
Baud rate = 1000 bauds per second (baud/s)
Bit rate = 1000 x 4 = 4000 bps

## Slide 3: Example:2
The bit rate of a signal is 3000. If each signal unit carries 6 bits, what is the baud rate?
Sol:
Baud rate = 3000 / 6 = 500 baud/s

## Slide 4
END..